# Synchronized Cooperative Broadcasting
The Synchronized Cooperative Broadcast (SCB) waveform was designed to transport primarily broadcast traffic within multi-hop mobile networks.
Precomputed SCB topology that mimics a static SCB network and allows us to fully model SCB’s cooperative effects. In this method we calculate the sum of receive power from transmitting nodes and compare that to a pathloss threshold (139 dB), to determine the set of nodes that are reachable, via multi-hop, from a given source node.
# Data files
Pathloss threshold 139 dB
Following data files include computed topology in a special case when the company is jammed from quite far away with free line of sight. The pathloss threshod is reduced with value 5 - 25 dB.
- 5 dB
- 10 dB
- 15 dB
- 20 dB
- 25 dB
# Connectivity graphs per company
# Company 1

# Company 2

# Company 3

# Company 4

# Company 5

# Company 6